## Slide 1: CORAL VER2
VERSION: A0
DATE: 28/12/2017

## Slide 2: Main issues
Project details and Supplies
Expected and required changes and Upgrades

## Slide 3: Order deliverables
Changes | Main notes | Abroad | Local | Unit
Wide Band Testability option Mech ( Nut Lock ) | 5675 – 5875MHz | V |  | BA-CB-TX5-SYS-HWT
Wide Band Testability option Mech ( Nut Lock ) Improve Ip1dB | 5675 – 5875MHz | V |  | BA-CB-RX18-SYS- HWHT
Mech ( Nut Lock ) ?? | 5150 – 5250MHz |  | V | BA-CB-TX5-SYS-L
Mech ( Nut Lock ) ?? | 5150 – 5250MHz |  | V | BA-CB-RX18-SYS- L

## Slide 4: Current System
Tx Power : 37dBm
Tx Antenna: 9.5dB
Rx antenna : 18dBi
  Frequency: 5.725 – 5.825GHz
  7MHZ BW
No Tx Near RX

## Slide 5: New System
Freq: 5675 – 5875MHz
Additional connection between site 1 and 2
3 Systems in same area
Scenario
  3 new systems
  Old system ( + additional Site 1-2 connection ) + 1 new system ( request that highest frequency will be 5850MHz)

## Slide 6: Frequency allocation Consideration
Rx IP1dB is~ -30dBm
Tx Rx antenna isolation is >50dB
Receiver selectivity:
  20MHz 50dB
  40MHz  90dB

## Slide 7: Freq Allocation Suggestion
In Old System Range
Chart: 
| 5675 | 5680 | 5685 | 5690 | 5695 | 5700 | 5705 | 5710 | 5715 | 5720 | 5725 | 5730 | 5735 | 5740 | 5745 | 5750 | 5755 | 5760 | 5765 | 5770 | 5775 | 5780 | 5785 | 5790 | 5795 | 5800 | 5805 | 5810 | 5815 | 5820 | 5825 | 5830 | 5835 | 5840 | 5845 | 5850 | 5855 | 5860 | 5865 | 5870 | 5875
SYS1 | 2 | 2 | 2 | 1 | 1 | 1 | 3 | 3 | 3
SYS2 | 2 | 2 | 2 | 1 | 1 | 1 | 3 | 3 | 3
SYS3 | 2 | 2 | 2 | 1 | 1 | 1 | 3 | 3 | 3

## Slide 8: Combining New and Old
NEW

## Slide 9: Additional NOTCH Filter
The RX in the new system require a Notch filter ( For Example)
  In opreder for Rx not to be “ specific For sit 2” a Bypass Switch Is needed.
Affecting Sensitivity in <2dB

## Slide 10: System drawbacks
All The Site 2 Transmitters have to be set to above 5820MHz
The RX in site 2 has to have a Notch Filter
If we Can increase Rx Ip1dB we can allow a more flexible solution.
  Increase IP1dB up to ~ 0dBm

## Slide 11: Increase IP1dB
Re Design Rf Front END
  Need IP1dB of ~0dBm
  NF Increase By ~ 4-5dB
In this case 40MHz Separation needed
Not replaceable with older unit

## Slide 12: Bit Option

## Slide 13: Required Functions
BIT of The link
Stop transmitting through Serial command
1w Output power
It is important to keep the low latency of the link!!

## Slide 14: Current Status
Data and Control are split into two Paths
Data does not pass through digital processing
This should also be the case with any system

## Slide 15: Offered Solution
Mux on transmitter to select data .
On Rx the unit is only Listening

## Slide 16: Painting Procedure

## Slide 17: Painting
color: Dark Green Lusterless no. 34052 per FED STD 595
Radom Painting Procedure
  - 1st step: Cleaning the surface with extra fine grade grinding sponge.
  - 2nd step: Cleaning the surface with chemical cleaner solvent.
  - 3rd step: Painting with EPOXY CHROMATE FREE Primer meeting MIL-PRF-53022 30-50 mic.
  - 4th step: Undercoat Painting EPOXY POLYAMID PER MIL-PRF-22750G Type II 24533 - Seafoam Green.
  - 5th step: Top coat Painting polyurethan per MIL-PRF-85285E Type II Class H Dark Green 34052. (UV protect

## Slide 18: PAINTING-OUR OFFER
We are Afraid for antenna performance.
We would like to do :
  polyurethane only paint system (no primer), where the plastic radomes is treated to accept the top coat

## Slide 19: Turning in the up/Down direction

## Slide 20: Summary of Changes

## Slide 21: Changes in Unit -Tx
Tx
  Should support 200MHz Band
    Replace PA Unit ( Need to Fix Power supply)
    Internal filter fix
    Replace output Filter
    Sw update
  Internal Bit
    Add CPLD
    Additional Functionality for BIT
    Option: Measure Voltage , temperature, Current?
  Paint

## Slide 22: Changes in unit - Rx
Rx
  Should support 200MHz Band
  Fix internal filters
  Fix Input BPF
  Add Notch filter
  Sw update
Internal Bit
    Add CPLD
    Additional Functionality for BIT
    Option: Measure Voltage , temperature, Current?
Paint