## Slide 1: SFC CDR
VERSION: A0
DATE: 1/11/2017

## Slide 2: Concept
The SFC converts the Ku band transmit frequency to the respective receive frequencies (2 RX Bands).
The Unit has single conversion with two options:
  From : 13.75GHz- 14.5GHz to 10.95- 11.7GHz
  From: 13.75GHz- 14.5GHz to 12.00- 12.75GHz

## Slide 3: SRR NOTES
Attached Word

## Slide 4: Mechanical Concept

## Slide 5: Mechanical concept

## Slide 6: Spec
Notes | Spec | Parameter | Section
V | 13.75-14.5GHz | Input Freq | 1
3-7dBi full band | 5 +/-1dBi | Rx Antenna | 2
V ( not at the same time) | Band 1: 10.95- 11.7GHz Band 2: 12.00- 12.75GHz | Output frequency | 3
V | 2.8GHz / 1.75GHz | LO | 4
V | Ip65 2 pole | Band Switch | 5
+/-280Hz , V | +/-0.1ppm | Freq Stability | 6
V | -80dBc @1KHz -90dBc @ 10KHz -100dBc @ 100KHz | LO PHASE NOISE | 7
3-7dBi full band | 5 +/-1dBi | Tx Antenna | 8
~V | -18dB +/-1dB | Rx To Tx antenna gain | 9
~V | -25dB +/-1dB | Input to output gain | 10
V | +/-1.5dB for full band +/-0.75dB for 80MHz | Gain Flatness | 11
V | +/-10deg for any 5MHz | Phase linearity | 12

## Slide 7: Spec cont
Notes | Spec | Parameter | Section
V | -40dBc | In band Spurs | 13
V | -40 dBm | Leakage Signals | 14
V | > 30dB | Image Rejection | 15
V | 0dBm | Input P1dB | 16
V | 5dBm | Damage power | 17
V ( problem to measure due to Network noise) | +/-0.5ns @ 40MHz | Group Delay | 18
Fixed after SRR to 90 deg | +/-10deg | 3dB Beam Width | 19
V see ICD | 7X 5.6 X 2.25 inch | Size | 20
V | 1A @ 12V DC | Power | 21
V ( three with Yellow) | 2 color LED | Visual indication | 22
V | Temp: -10 to +55 deg Rain : Drops Humidity : 10 – 95% | Environment | 23
Updated to another option according to letter from 30/7/2017 | Alodine | Coating | 24

## Slide 8: Spec cont
Notes | Spec | Parameter | Section
V | PT02E10-6P | Power Supply connector | 25
At Risk currently at 1Kg | <0.6Kg | Weight | 26

## Slide 9: Block Diagram

## Slide 10: System Simulation

## Slide 11: System Simulation

## Slide 12: Input Filter

## Slide 13: Mid Filter
Additional filter For 13.75-14.5GHz

## Slide 14: Mixer
SIM-193H+
Need Passive mixer to allow for the specific operation Where:
Rf : 13.75GHz – 14.5GHz
IF : 10.9 -12.75GHz
LO: 1.75 – 2.8GHz
Use Mixer and switch IF and LO Connection

## Slide 15: Mixer Preliminary tests
Expected Spurs
Multipliers of LO :
  1.75GHZ  6,7,8X == 10.5GHz, 12.25GHz, 14GHz
  2.8GHz  4,5X == 11.2GHz , 14GHz
  All Should be below -40dBm
  Function of LO input
Signal relative spurs are not expected

## Slide 16: Output Selectable filters
Two Bands
Bank filters
Option of bypassing both filters

## Slide 17: Output Filter

## Slide 18: LO Stability OCXO
Tuning Option available

## Slide 19: Lo Phase Noise
ADF4351
Phase Noise Table
Spec | Phase noise 1.75GHz | Phase noise 2.8GHz | Freq
 | -90dBc/Hz | -85dBc/Hz | 100 Hz
-80dBc/Hz | -95dBc/Hz | -95dBc/Hz | 1KHz
-90dBc/Hz | -99dBc/Hz | -96dBc/Hz | 10KHz
-100dBc/Hz | -106dBc/Hz | -106dBc/Hz | 100KHz
 | -130dBc/Hz | -130dBc/Hz | 1MHz

## Slide 20: Amplifier – CHA-3656QAG
Optional Both on input and Output
Allows option of controlling the Spurs

## Slide 21: Antennas
Frequency : 10 -15GHz
Use Std Coax to Waveguide
Measured in Lab
Pr / Pt = Gr Gt λ² / (4π)² R²

## Slide 22: Waveguide to MS

## Slide 23: Waveguide to Coax
Built from waveguide to MS and Then MS to Coax

## Slide 24: Power Consumption
NOTES | Current | Voltage | Unit
Startup only | 1A | 3.3 | OCXO
 | 0.2A | 3.3 | LO
 | 0.06A | 3.3 | LO Buffer
 | 0.12A | 3.3 | LNA/RF AMP
 | 1.4A From 3.3V | Total | 
From 12V to 3.8V
Ldo used down to 3.3V

## Slide 25: Schematic
2 RF BOARDS
  RF PATH
    Filters + MIXER +AMP
  DC /PIC/ OCXO SYNTH

## Slide 26: RF SCHEMATIC

## Slide 27: RF Schematic – input

## Slide 28: RF SCHEMATIC - OUTPUT

## Slide 29: RF PCB
RO4350B 0.254mm
No coating on Filters – only Copper

## Slide 30: Main Control Board

## Slide 31: DC/PIC

## Slide 32: SYNTHSIZER TOP LEVEL

## Slide 33: Synthesizer

## Slide 34: PC BOARD
FR4 HIGH TG , 1.6 mm
4 Layers

## Slide 35: SW
Using Pic PIC16LF1823-I/ML
SW SPI To control Freq
According to Sw state will control Switches and SPI
Control 2 pins for LED

## Slide 36: Down Converting to LBAND Option
Changes :
  Need to Replace AD4351 with ADF5355
  Need to switch between input ports for the Mixer
    Better Way to add additional mixer and switch LO

## Slide 37: Mechanical

## Slide 38: Mechanical Model
EDRAWING
Currently 1Kg

## Slide 39: Connectors

## Slide 40: Switch/LED
M2012LL3G01

## Slide 41: External Cable
Cable Types
Alpha Wires
  PART NO. 78033
  PART NO. 78043
AC/DC - LPF-16-12P

## Slide 42: Schedule
NOTES | DATE | MILE STONE
 | 1/11/2017 | CDR
 | 15/11/2017 | Prototype blocks
 | 15/12/2017 | Final Mech,PCB order
 | 1/3/2018 | First unit ready
Might be sooner | 1/5/2018 | ENG UNIT

## Slide 43: Risk