## Slide 1: KU FE Module ( Demo Project)
VERSION: A3
DATE: 11/11/2017

## Slide 2: Concept
TDD Unit
Two Antenna System ( TX, RX)
Tx : From 950 – 2620 MHz to 10.95 – 11.7 GHz
Rx : From 13.75 – 14.5 GHz to 950 – 2620 MHz
Tx Output of 36dBm @ 5dB backoff
Time Critical !!

## Slide 3: Block Diagram

## Slide 4: SPEC-Tx
Comply | Notes | Spec | Parameter
V | 2570-2620MHz For this demo | 950-2620MHz | L-Band input Freq
 |  | -10 to -50dBm | Power Input
 |  | 10.95 – 11.7GHz | Ku band output
V | -30 to 55 deg cel | +/-0.5dB over temp range | Gain Stability
 |  | -50dBc/Hz@ 10Hz | Phase Noise
 |  | -66dBc/Hz @ 100Hz | 
 |  | -80dBc/Hz @ 1KHz | 
 |  | -90dBc/Hz @ 10KHz | 
 |  | -90dBc/Hz @ 100KHz | 
 |  | -104dBc/Hz @ 1MHz | 

## Slide 5: SPEC-Tx
Comply | Notes | Spec | Parameter
V |  | 50dBc | Harmonics
V | Non carrier related | -60dBm in band | Spurious
V | Carrier related | -60dBc in band | 
V | 5dB backoff | 36dBm min | Output power
V |  | 12dB min | Gain Control
V | LTE Signal | 30dBc @36 dBm output | Spectral regrowth

## Slide 6: SPEC-Rx
Comply | Notes | Spec | Parameter
V | 2570-2620MHz For this demo | 950-2620MHz | L-Band output Freq
 |  | 13.75 – 14.5GHz | Ku – band input
 |  | 4 dB max | NF
 |  | -15dBm min | IIP3
 |  | -25dBm min | Ip1dB
 |  | +5dBm min | Max in power for burn
 |  | 20dB +/-1dB | Total Gain
 |  | +/-0.5dB | Gain Stability
 |  | Same as TX | Phase noise
Only in IF low BW and not in full band |  | 50dBc min | Harmonics

## Slide 7: SPEC-Rx
Comply | Notes | Spec | Parameter
V | Non carrier related | -60dBm in band | Spurious
V | Carrier related | -60dBc in band | 
 |  | 4.5 us | Switching Speed Tx/Rx

## Slide 8: SPEC
Comply | Notes | Spec | Parameter
 |  | Tx Full VSWR Protection Rev voltage protection | Protection
 |  | Tx output power PLL Lock PA Temperature IF input power ( option) Tx Return power | Monitor
 |  | 18-36V | DC
 |  | 45W max at TX mode | DC Power
 |  | Mil-STD-704 , Mil-STD-461E | DC Protection
For OCXO Stability |  | 60 sec | Turn on time

## Slide 9: Tx

## Slide 10: Block Diagram

## Slide 11: BA1478_UP
Used As is
The TGC2510-SM
  Gain change of 18dB ( 0 V ) to 0dB ( 2V)
  At High Gain OIP3 =~30dBm but at Low gain ~25dBm
  Switch Vgate Levels at RX Mode.
MGA-53543
  Always on
Requires no RF input while not in Tx mode .

## Slide 12: BPF
10.95-11.7GHz

## Slide 13: PA – 2X TGA2760-SM
Gaas with PA GAN
Combine 2 units for better matching , linearity , heat dissipation
Switch Gate Voltages to shut down
Requires turn on Sequence

## Slide 14: LPF
Microstrip LPF
On RO4350B , 10 mil , 0.5 oz
No coating or plating of PCB copper

## Slide 15: Circulator
Optional as Balanced operation should do the job
No Data on PA capability to withstand VSWR
Circulator will allow monitoring REV power.
This is not a must and will be an option

## Slide 16: Monitoring TX
BA1478_UP
  ADF5355 Lock Detect
Amplifier has internal Detector for FWD power
Read Rev power
Temperature sensor near PA
28V current and voltage monitor.

## Slide 17: RX

## Slide 18: Block Diagram

## Slide 19: RX – Limiter (Optional)
Currently not planned to be placed
TGL2217-SM

## Slide 20: BPF
1097L470-001
Can Add XLF-173+ LPF

## Slide 21: LNA
Custom Design Not using Std Devices
  Non STD Narrow Band 13.75-14.5GHz
  Required Low NF
Risk Ip1dB , Input for burn not knowm
Based on CEL CE3521M4
Fall Back On CHA 2066-QAG
  NF: 2.5-3 dB
  Pin max = -3dBm

## Slide 22: BA1478_DOWN
Only TGC2610 –SM on RF Path
  +Synth
  Eliminate Additional IF Amp
  IF BPF is a PCB Fix .

## Slide 23: SYNTH AND CLOCK

## Slide 24: Synthesizer
ADF5355
  Placed on BA1478 units
  Controlled By MCU
What is the Synth Step ?
  10,20MHZ ?
With 20MHz OCXO and 20MHz Steps

## Slide 25: DC

## Slide 26: Power Users
 | On mode | Current [mA] | Voltage [V] | Unit
 | All | 800 | 5.5 | BA1478_up
 | TX | 2200 | 7 | PA PRE
 | TX | 2000 | 28 | PA
 | ALL | 3 | -1 | PA VG 1
 | ALL | 3 | -3 | PA VG 3
 | ALL | 20 | 3.3 | LNA
 | ALL | 300 | 5.5 | BA1478_down
 | ALL | 200 | 3.3 | MCU
1000 @ startup | ALL | 300 | 3.3 | OCXO

## Slide 27: Power Scheme

## Slide 28: Power Supply units ( Non Isolated)
Operating | On mode | Current [mA] | Max Current [mA] | Voltage [V] | Unit
PA | DC/DC Buck Boost | 2000 | 2700 | 28 | MGDS-75-H-J /PI3749-00-LGIZ
PA | Dc/DC | 2500 | 3500 | 7 | TPS54340
ALL ( up/Down converter) | DC/DC | 3200 | 3500 | 5.5 | TPS54340
MCU | LDO | 200 | 250 | 3.3 | TPS73233DBVT
OCXO | LDO | 1000 | 1100 | 3.3 | LT1965EDD-3.3#PBF
LNA | LDO | 150 | 150 | 3.3 | ADP150AUJZ-3.3-R7
PA BIAS | INV LDO | 6 | 10 | -4 | MAX881REUB

## Slide 29: Power Supply Pulses
Supporting pulses will require large capacitors
A turn on sequence will be set inside device
  5.5v turns on before others
  Only when negative voltage in +/-5% 28,7V go to the PA

## Slide 30: MCU

## Slide 31: Required Function and Pins
 | Description | # PINS | Function
 | SPI FOR ADF5355 | 4 | PLL UP
Can be only CE | SPI FOR ADF5355 | 4 ( 1) | PLL DOWN
For PA Bias | SPI for Dual DAC | 5 | AD5312
For UP Gain | SPI for Dual DAC | 5 | AD5312
 | Analog Inputs | 6 | Temp, FWD, REV, Voltage, Current
 | UART Com RS422 | 2 | UART IN/OUT
 | Discrete OUT | 2 | LED
 | Discrete OUT | 5 | Power ENABLE
 | Input to monitor TX/Rx ( interrupt) | 1 | TX/RX Monitor

## Slide 32: Layout

## Slide 33: Layout consideration
All RF On RO4350B 10 mil 0.5oz/oz
Filters and coupler with no plating
Built from Separated building blocks
POWER/COM/MCU will be on FR4 in Separated Board
ANTENNA SIZE?
ANTENNA CONNECTOR

## Slide 34: First Placement

## Slide 35: Mech

## Slide 37: Schedule

## Slide 38: Mile stones
 | Notes | Date | Mile Stone
 |  | 20/11 | CDR
 | BA1478 ready | 15/12 | PCB Ready for production
 |  | 15/12 | Mech ready for production
 | RF Connectors might be LLI | 15/12 | All Parts in B.A.
 |  | 27/12 | PCB Assembly
 |  | 1/1/2018 | Mech in B.A.
 |  | 15/1/2018 | Finish RF Design
 |  | 28/1/2018 | SW Control Integration
12 weeks from 31/10 ARO |  | 28/1/2018 | ENG UNIT
 |  | 25/3/2018 | SOF
 |  | 15/4/2018 | 4 PROTOTYPES

## Slide 39: RISK